## Slide 1: Research Topic and Objectives
Topic | Which GB market product rules made grid-scale batteries profitable, and how much does each rule change revenue and operation? | 
Question | What we want to find out | Method
RQ1 Revenue evolution | How the battery revenue mix changed from 2020 to 2026, and which rule changes defined each phase | Revenue-stack decomposition from public data; rule timeline
RQ2 Rule attribution | How much each rule (fast frequency response, EAC co-optimisation, SoE rule, reserve products, BM access) contributes to revenue, and whether this differs between phases | Rule on/off counterfactuals in an optimisation model; Shapley decomposition
RQ3 Operating strategy | How optimal bidding and operation (service allocation, cycling, state of energy) change when rules change | Perfect-foresight vs rolling-horizon MILP
Benchmark Realised revenue | How far actual battery revenue falls below the model upper bound | Unit-level revenue rebuilt from public EAC, BM and wholesale data

## Slide 2: GB Market Phases
Phase | Period | Key rule changes | Battery revenue
1 Contracted Entry | 2016 – Sep 2020 | Enhanced Frequency Response tender (2016, 4-year contracts); Firm Frequency Response; Capacity Market | First commercial batteries on fixed-term contracts
2 Scarcity Boom | Oct 2020 – 2022 | Dynamic Containment launched (price cap £17/MW/h); DC + BM stacking allowed (2021); DM and DR (2022) | Frequency response ≈ 90% of revenue
3 Saturation and EAC | 2023 – 2024 | DC prices fall by over 90%; EAC co-optimised auction (Nov 2023); Balancing Reserve and 30-min rule (Mar 2024); SoE rules (2024); Quick Reserve (Dec 2024) | Shift to wholesale + BM; ≈ £50k/MW/yr in 2024
4 Merchant and Dispatch Reform | 2025 – present | Quick Reserve open to non-BM units (Sep 2025); BR moves into EAC (Oct 2025); Slow Reserve (Mar 2026); GC0166 BM parameters | Wholesale + BM ≈ 60%, ancillary ≈ 1/3, Capacity Market ≈ 10%
The model compares pre-EAC (2021 – Oct 2023) and post-EAC (Nov 2023 onwards) conditions with the same engine.
Revenue shares: Modo GB index, indicative.

## Slide 3: Modelling Approach and Rationale
Modelling choice | Rationale
Perfect-foresight MILP (first layer) | Gives the revenue upper bound; losses from imperfect information (rolling horizon) and BM non-acceptance are measured against it
Price-taking battery, 50 MW / 2 h | A single unit barely moves prices; 2 h is the dominant new-build duration (1 h and 4 h as scenarios)
30-min periods; DC/DM/DR fixed per 4-h EFA block | Matches GB settlement and the auction product definitions
Wholesale price: Elexon MID | Free and public; also used by the closest Q1 study (Gale et al. 2026), so results are comparable
Revenue: wholesale + EAC services | DC/DM/DR and BR/QR/SR can be stacked with trading in the same period; BM and Capacity Market are added as later layers
Headroom and energy constraints | Services must be deliverable: power margin around the baseline, energy for the contracted duration (2024 SoE rule), energy drawn by frequency response
Charge/discharge binaries | Prevent simultaneous charging and discharging at negative prices
Rule switches + Shapley decomposition | Attribute revenue to each rule; Shapley averages over all orderings because rules interact